This page was exported from Trinco Trinity Tool Co. [    http://trinco.com    ]

Export date: Thu Apr 18 19:44:14 2024 / +0000 GMT

# TRINCO™ MODEL 40x40 SPLIT LEVEL DIRECT PRESSURE with DP850

Product Categories: Direct Pressure Systems

Product Tags: Cabinet Size: 40x40

Product Page: https://trinco.com/product/direct-pressure-split-level-40-x-40-dp850/

## Product Summary

TRINCOTM 40X40 SPLIT LEVEL DIRECT PRESSURE CABINET

A TrincoTM direct pressure cabinet utilizes an A.S.M.E. coded pressure pot to hold abrasive media. When the foot pedal control is depressed, air pressure is released into the pressure pot, pressurizing the pot and then forcing the media from the pot through the blasting hose to the nozzle.

Most TrincoTM pressure blast cleaning is done at 40-60 PSI. Due to these lower pressures, abrasive media breakdown is greatly reduced even though a high volume of media is being directed at the part to be cleaned. Most of the media is recovered through the recycling process.

TrincoTM Direct pressure blast cleaning is ideal for the very tough jobs, for applications where large surfaces must be cleaned quickly, for production blast cleaning or when the job requires the use of heavy mesh sizes of silicon carbide, aluminum oxide, garnet, etc.

Other popular medias that are used in TrincoTM pressure cabinets are glass beads, Trin-mixesTM, Rad-mix, and plastic blast cleaning media.

## Product Short Description

### Equipment Features

TrincoTM Abrasive separator is constructed of 10 gauge welded steel for durability and is tuneable for different media

TrincoTM Cabinet is constructed of 14 gauge welded steel.

ASME Coded pressure vessel with easy access clean out port, automatic sealing plunger, and pneumatic vibrator

¾” Piping and heavy duty mixing valve

30 - 120 PSI pressure range

Abrasive capacity - 100 Lbs standard

TrincoTM Vibrating particle screen in abrasive separator

Includes:

TrincoTM Fluorescent lighting

Airline water filter

Pressure regulator and gauge

Neoprene blast gloves

TrincoTM Safety enclosed foot pedal

TrincoTM ½” ID heavy duty blast hose

TrincoTM Tungsten carbide nozzle

TrincoTM ¼” ID nozzle standard, 1/8”, 3/16” and 5/16” optional

### Specifications: Dust Collector

TrincoTM Pull through type dust collector with motor and impeller on clean air side

Includes 30 TrincoTM Tubular filter bags (145 Sq ft. surface area)

Trinco manual bag shaker

### Abrasive Separator:

Rated 850 CFM

Motor: 2HP

3450 R.P.M.

230V, 1 Phase, 60 HZ

### Inside Dimensions:

DEPTH: 40”

WIDTH: 40”

HEIGHT: 31”

### Overall Dimensions:

DEPTH: 66”

COMPLETELY OPEN: 71”

WIDTH: 44” HEIGHT: 71”

### Door Openings:

SIDE DOOR: 20”x 30”

FLIP TOP: 40”x 40”

FLOOR SPACE INCL.

DUST COLLECTOR: 96”x 71”

SHIPPING WEIGHT: 1400 LBS.

*Note: This unit is designed to handle most standard media

Please specify type and size of media when ordering

Product added date: 2016-05-03 19:30:35

Product modified date: 2017-05-12 15:06:44

Product export as MS Document by WooCommerce PDF & Print plugin.